## Slide 1: Some three letter acronyms
There are two types of schedule providing market information to participants within 36 hours of real-time. Both schedules are run in parallel to allow participants to compare the results:
NRS: Non-response schedule. A market schedule that presumes the only price sensitivity of demand will be dispatchable demand bids
PRS: Price response schedule. This schedule includes the price information contained in industrial load demand bids and difference bids
For the purposes of this explanation, we will also introduce:
DDC: discretionary demand control. The emergency demand control that distributors will be signalling that is available to the system operator under a grid emergency

## Slide 2: A timeline of market schedule signals
System operator requests DDC availability (up to 24hrs ahead)
If forecast schedules indicate DDC will be necessary
Dispatch (assuming DDC is required under a Grid Emergency)
NRS: prices “normal”
PRS: prices “normal”
Additional PRS information:
Both price and total MW volume of difference bids visible to participants
NRS: scarcity prices ($10k/MWh)
PRS: difference bid price (assuming DDC is required and adequate to mitigate shortfall, if DDC is inadequate then scarcity prices will result)
First dispatch schedule: DDC requirement will show as energy shortfall and scarcity price will result ($10k/MWh) and SO will require DDC use
Next dispatch schedule:
DDC MW will be added back to the actual load measurement to derive price outcome. If still insufficient generation, scarcity pricing will persist until actual load plus DDC falls to a level that can be supplied by the available generation